## Slide 2
Reliability Testing Dataset
(Test-to-failed data)
Distribution Fitting with MLE method
(Weibull, Lognormal, exponential)
MTTF Calculation &
Survival Rate Function
Statistical Model Validation
through K-S test & p-value validation
Uncertainty Quantification
(Bootstrap, Stochastic)
Technical Report
(Automated Output)
Find the statistical model that best represents actual failure behavior
AI-powered prompting workflow
AI generates the fitting program code
Engineers manually debug and verify it.
Transform statistical results into lifespan
AI-powered quantify product longevity provides a basis for reliability and warranty strategies.
AI automatically substitutes parameters into formulas (such as Weibull: η×Γ(1+1/β)) and generates textual and graphical explanations.
AI integrates technical report interpreting with charts and parameter values
The large language model (LLM) automatically generates descriptions and engineering insights for each figure, ensuring clarity and readability for all users.
Estimate the distribution stability and confidence level of the parameters through repeated simulations or sampling
All models have uncertainties, repeated sampling (bootstrap) is used to improve distribution stability
AI simulates and builds stochastic models to accelerate computation, automatically outputs confidence level diagrams.
Verify whether the model truly reflect actual failure behavior
Kolmogorov–Smirnov (K-S) Test: Compares the simulated distribution with actual data.
p-value verification: If p > 0.05, it indicates that there is no significant difference between the model and the measured data, and the model is acceptable.
AI automatically interprets the test results. If the p-value is too low, it generates a warning and suggests an alternative distribution.
Notes: 以 Emperor Pan and tilt 為例